## Slide 1
Aamir Suhail Burhan
Graduate Student, Department of Electrical & Computer Engineering
University of Colorado Boulder
RISC-V 5-Stage Pipeline Processor

## Slide 2
Agenda
Introduction
Design
Behavioral Simulation
Challenges Faced
Work Breakdown Structure
Learnings & Conclusion

## Slide 3
1. Introduction
RISC-V is an Instruction Set Architecture established using reduced instruction set computer (RISC) principles.
Tools - Vivado 2023.2
Language - Verilog
Hardware - NEXYS A7 100T
Validation - Vivado Simulator [Behavioral Simulation]

## Slide 4
2. Design

## Slide 5
2.1. Instruction Fetch Stage

## Slide 6
Types of Instructions Implemented:
1. Register Type
2. Immediate Type [Add & Load]
3. Store Type
2.2. Instruction Decode & WriteBack Stage

## Slide 7
2.3. Execute Stage

## Slide 8
2.4. Memory Stage

## Slide 9
3. Behavioral Simulation( z[0] = a*x[0] + y[0])
Values Loaded Into Instruction Memory at reset:
1. Add Immediate Value of a into R9: 0000000 00011 00000 000 01001 0010011 [0x00300493]
2. Load Value of x[0] into R1: 0000000 00000 00000 010 00001 0000011 [0x00002083]
3. Load Value of y[0] into R2: 0000000 00001 00000 010 00010 0000011 [0x00102103]
4. Multiply 'a * x[0]' Result in R8: 1111111 00001 01001 000 01000 0110011 [0xFE148433]
5. Add y[0] + R8, Result placed in R5: 0000000 00010 01000 000 00101 0110011 [0x002402B3]
6. Store R5 Result in Memory: 0000000 00101 01010 010 00000 0100011 [0x005022A3]

## Slide 10
3. Behavioral Simulation
NOP????

## Slide 11
3. Behavioral Simulation( z[0] = a*x[0] + y[0])
Values Loaded Into Instruction Memory at reset:
1. Add Immediate Value of a into R9: 0000000 00011 00000 000 01001 0010011 [0x00300493]
2. Load Value of x[0] into R1: 0000000 00000 00000 010 00001 0000011 [0x00002083]
3. Load Value of y[0] into R2: 0000000 00001 00000 010 00010 0000011 [0x00102103]
4. NOP x 2
6. Multiply 'a * x[0]' Result in R8: 1111111 00001 01001 000 01000 0110011 [0xFE148433] {a = 3, x[0] = 6}
7. NOP x 3
10. Add y[0] + R8, Result placed in R5: 0000000 00010 01000 000 00101 0110011 [0x002402B3] {y[0] = 8}
11. NOP x 3
14. Store R5 Result in Memory: 0000000 00101 01010 010 00000 0100011 [0x005022A3]

## Slide 12
ADDI R9, R0, 3
LW R1, 0(R0)
LW R2, 1(R0)
MUL R8, R9, R1
ADD R5, R2, R8
NOP
NOP

## Slide 13
MUL R8, R9, R1
SW R5, 5(R0)
NOP
NOP

## Slide 14
4. Challenges Faced
Initial Design Involved Using DDR2 present on the NEXYS Board
Timing Closure Issues

## Slide 15
5. Work Breakdown Schedule
M3.1
M3.2
M3.3

## Slide 16
6. Learnings & Conclusion
Understood the RISC-V ISA in a detailed manner by implementing a basic version of the processor design.
Realization of the performance improvements the concept of Forwarding provides.
Complexity of meeting timing requirements to avoid data hazards.
Importance of a compiler to provide instructions which improve speed was better understood.

## Slide 17
Thank You!